#### Contents

Introduction

Safety

Cleaning

Connections

Cartridge gain and loading

Technical specification –

Fig.1	Rear panel connections

Fig.2	Basic audio connection

Fig 3	Gain and load selector

Warranty

Note –  CAUTION  -

A GAIN VALUE MUST BE SELECTED BEFORE SWITCHING THE UNIT ON.

IF NOT YOU WILL DAMAGE THE UNIT!!

Introduction

Thank you for purchasing the Whest Audio phonostage.

As you know, this unit is designed to retrieve the maximum amount of information from your vinyl LPs.  It does this by using proprietary low noise/ high current audio circuitry as well as our proven hybrid filtering enables the TITAN PRO II to playback up to approximately 60Khz with ease.

Brief history

The RIAA curve was designed many years ago to enable the use of vinyl as a playback medium.  Back then the humble stylus and audio electronics could really only playback a very limited bandwidth.  A system bandwidth of 12Khz was quite rare.  Nowadays most systems have a bandwidth of 100Khz; the modern day cartridge can playback frequencies beyond 60Khz – so why continue to use a phonostage with a filter curve designed for systems designed in the 1950s?

Forward thinking

Because of our close links with the music recording industry we were able to measure several Neumann cutter heads prior to cutting a master onto acetate.  What we found was that the cutter head would cut high frequency all the way to 50Khz!

With these results and the research acquired from the DAP programme we then designed a hf filter that would complement the RIAA filter we had designed for the MC REF V.  This has been incorporated into the TITAN PRO II phonostage.  Because of the extended hf response of the TITAN PRO II phonostage, large amounts of information are now able to be heard when it was once thought there was nothing there!

The extended hf enables you to hear further into the soundstage by bringing to life the lowest frequencies of a kick drum and positioning all instruments to form a three dimensional soundstage.

The TITAN PRO II also incorporates some new and unique technology which enables the phonostage to occupy the same case as the transformer without the need of a separate box.  This means the critical electronics can now utilise the ultra stable, low noise and high speed power source in an instant – no delay lines!  This translates into a lower noise floor, far better micro detail resolution, far better image stability and soundstaging which will bring you closer to the recording.

The TITAN PRO II is the first in whole new breed of phonostages from the Whest Audio stables.

Note –  CAUTION  - A GAIN VALUE MUST BE SELECTED BEFORE SWITCHING THE UNIT ON.        IF NOT YOU WILL DAMAGE THE UNIT!!

Safety

Place your unit on a firm level surface where it is not exposed to dripping or splashing of any liquid.  Position it away from radiators and other heat sources and leave a space of at least 5cms around the unit for ventilation.

Please note that there are no user serviceable parts inside.

In the unlikely event that this unit needs to be serviced please return it to an authorised Whest Audio service agent.

There is a risk of electrical shock if this unit is opened!

Please do not attempt to open this unit for servicing or modification unless authorised as it WILL invalidate your warranty.

Cleaning

When cleaning the unit please do not use any liquids as it may enter the unit causing it to malfunction.  We recommend applying a very small amount of engineering oil such as WD40® to a lint free cloth and then wipe the unit in the direction of the grain on the lid.

Engineering oil is a tried and tested method of cleaning grained aluminium panels.  You only need to do this a few times a year.  The other parts of the TITAN PRO II case maybe cleaned with a damp/near dry cloth or a non-silicone based polish applied to a non-abrasive sponge.

Connections – BEFORE SWITCHING ON… YOU MUST SELECT A GAIN VALUE.

Please read the safety section before connecting your unit.

Before connecting to the mains, check that the mains supply voltage corresponds to the voltage printed next to the power inlet.  If the mains voltage is different, please consult your authorised Whest Audio dealer.

All TITAN PRO II units come supplied with an Audiophile grade interconnect as well as a computer grade interconnect for transferring your LPs to your computer.

Although all listening tests were conducted with this interconnect please feel free to use your preferred interconnect or ask your dealer for advice.

1.	When connecting the TITAN PRO II please make sure that your system’s source selector is switched to an input OTHER THAN the input to which the TITAN PRO II unit is to be connected.

2.	Please make sure that the TITAN PRO II phonostage unit is connected to a switched wall socket or similar switched socket using an appropriate power lead and is in the OFF position.

3.	First disconnect the turntable from the amplifier/preamplifier or other phonostage.

MAKE SURE YOU HAVE SELECTED A GAIN VALUE BEFORE ANYTHING ELSE !!

4.	Connect the turntable leads to the TITAN PRO II phonostage observing the colour codes for channel ID.

5.	Connect the ‘grounding’ lead from the turntable arm lead to the grounding post on the TITAN.

6.	Connect the output of the TITAN PRO II to the amplifier/preamplifier aux/line input.

7.	Once you are happy that all inputs and outputs have been connected properly, switch the power on- on the wall socket and then switch the TITAN PRO II on via the rear panel on/off switch located next to the power inlet.

8.	If all is OK, just switch on.  A small RED LED will glow on the front panel of the TITAN PRO II phonostage – this indicates that all is OK.

10.	Select the correct source input on the amplifier/preamplifier.

11.	You are now ready to enjoy, so, play an LP, sit back and take it all in.

It may take several hours before the TITAN PRO II phonostage settles down to work efficiently, but generally 6-12 hours is sufficient time for the sensitive components to find their ‘steady state’ working temperature.

The TITAN PRO II phonostage has been designed to be simple to integrate into any audio or computer based system.

Please familiarise yourself with the rear panel layout Fig. 1 as it will make connecting, unplugging and cleaning easier.  For basic connectivity follow Fig. 2.

Connecting to a computer soundcard for transferring to hard-drive

The TITAN PRO II phonostage comes supplied with a special interconnect to connect to your computer soundcard analog input.  With this interconnect and using the Whest Audio recommended software http://audacity.sourceforge.net/download  (or as a download from our website – www.whestaudio.co.uk)  you will be able to transfer your vinyl collection to your computer hard drive.

The TITAN PRO II can be connected to your computer sound card analogue audio input while the TITAN PRO II and computer are in the ‘on’ position.

Once connected install the correct software for your computer system (MAC or Windows).   http://audacity.sourceforge.net/download/

Follow the on-screen instructions and read the instructions in the help files or online at www.whestaudio.co.uk .  The help files also contain information on how to maximise the software’s capabilities with regard to editing, etc.  In case of any transferring problems, please check the help files.   To get the best possible quality from your transfers please do read the instructions fully before attempting to transfer your vinyl.

Cartridge gain and loading (Fig. 3)

Caution: THIS OPERATION CAN ONLY BE DONE WHEN THE UNIT IS DISCONNECTED FROM BOTH THE MAINS POWER SUPPLY AND THE AUDIO SYSTEM –

Your TITAN PRO II comes preset for a moving coil cartridge requiring a gain setting of 64dB and a load setting of 100ohms.  This will be fine for the majority of moving coil cartridges.  If however your cartridge requires a different setting you can either ask your dealer to set it for you OR you can easily do it yourself in just a few minutes:

- A small 3mm allen key driver is used to remove the 2 screws holding down the access panel underneath to get access to the gain and load settings.  (Fig. 3)

ii)	place the TITAN PRO II upside down with the 4 switch banks at your top left.

iii)	you will notice a 4 x RED 8 position switches near the gold RCA socket end.  These switches control the gain and loading characteristics.  There are 2 x  8 way switches per channel.  As mentioned previously the unit is supplied set up for MC64/100ohms (64dB gain and 100ohm load).  Note MC gain starts at 50dB.

iv)	look at the switch and you will see an ‘on’ position

- to set the TITAN PRO II for moving magnet with a load value of 47K ohms:

- set all the switch positions to the ‘off’ position

- slide GAIN switch no. 1 indicating 40dB and LOAD switch no. 8 indicating 47kohms (MM)

- to set the TITAN PRO II for moving coil with a output value of 0.25mV

- set all the switch positions to the ‘off’ position

- slide GAIN switch no. 6 indicating 64dB and LOAD switch no. 1 indicating 100ohms (MC)

v)	once your gain and load characteristics are set, just place the panel back on then replace the 2 screws.

If your cartridge requires a different loading value, please ask your Whest Audio dealer or contact Whest Audio Ltd on whestworld@fastmail.fm or tel: +44 (0) 20 3 176 0376

Alternatively, if you find that you have just purchased a cartridge that requires gain and load values outside of the parameters used by any other phonostage manufacturer, please call Whest Audio Ltd on +44 (0) 20 3176 0376 or email whestworld@fastmail.fm .  Our technical department will be able to advise how to setup the TITAN PRO II phonostage for your new cartridge as the unit has the ability to be ‘trimmed’ for absolutely any cartridge manufactured via the ‘user’ load setting.

Whilst changing the load and gain settings, the lid and/or front panel may end up covered with fingerprints – please read the section on cleaning to bring the TITAN PRO II phonostage up to its former glory!

Technical specification

Model No.:	TITAN PRO II dual mono phonostage

RIAA curve accuracy:	17Hz – 20.5Khz  +/- 0.15dB or better

Frequency response:	5Hz – 65Khz  +/- 1.0dB

Working band:	15Hz – 58Khz

MM Gain:	42dB  @ 47Kohm

MC Gain:	50dB - 76dB to suit all 0.10 – 0.7mV cartridges

Cartridge Loading	30ohm - 47Kohm in 8 steps plus ‘USER’

THD+N:	0.0018%

Connections:	Unbalanced RCA, Impedance Balanced on 3-XLR

Connectors:	Audiophile GOLD RCA,

Unpacked weight:	7.0Kgs

Packed weight:	8.5Kgs

Dimensions:	1 x 480mm x 300mm x 83mm

Operating voltage:	230VAC 50Hz or 115VAC 60Hz (see dealer)

Supplied in package:

1 x TITAN PRO II dual mono phonostage

1 x Audiophile RCA interconnect

1 x Audiophile 3.5mm plug to 2 x RCA computer/ audio cable

1 x IEC power cable

Warranty

All Whest Audio products are covered by a limited warranty against defects in design, materials and workmanship for a period of FIVE (5) years from the original date of purchase to the original purchaser only.  This warranty is available upon proper registration of ownership within thirty (30) days of first purchase.

Proper registration is made by filling out and returning the attached warranty registration card along with a copy of the original sales receipt as proof of the original date of purchase.

If during the warranty period this product fails to operate under normal use and service due to defects in design, materials or workmanship, Whest Audio will, at their option, either repair or replace the product in accordance with the terms and conditions stipulated herein.

Whest Audio reserves the right to charge a handling fee if a returned product is found to be not under warranty, according to the conditions below.

Warranty Conditions

1.	This limited warranty is valid only if proper registration of this product is made in the way described above.

2.	If Whest Audio repairs or replaces the product, the repair for the defect concerned, or the replaced product shall be warranted for the remaining time of the original warranty or for ninety (90) days from the date of repair, whichever is longer.

3.	This warranty does not cover any failure of the product due to normal wear and tear, or due to misuse, including but not limited to use in other than the normal and customary manner, in accordance with the Whest Audio instruction for use and maintenance of the product.  Nor does this warranty cover any failure of the product due to accident, modification or adjustment, acts of God or damage resulting from liquid.

4.	This warranty does not cover product failures caused by modification or repair of the product performed by a non-Whest Audio authorised person.

5.	In no event will Whest Audio Limited be liable for incidental or consequential damages of any nature whatsoever arising from purchase, use or inability to use this product.

6.	There are no express warranties, whether written or oral, other than this printed limited warranty.  All implied warranties, including without limitation the implied warranties of merchantability or fitness for a particular purpose are limited to the duration of this limited warranty.

The warranty does not affect the consumer’s statutory rights under applicable legislation in force.

Please complete the Warranty Registration Card and send it together with a copy of the original sales receipt to:

WHEST AUDIO LIMITED

WARRANTY REGISTRATION DEPARTMENT

Q West  Suite 2.07

Great West Road

London  TW8 0GP

For your records:

Model                ………MC TITAN Pro II  ………………………………………………………….............

Serial No.  	……#TP II……………………………………………………………………………...………

Purchase Date   …………….	………………………………………………………………………………………...…...

Supplier  	……………………………………………………………………………………………………………..

For OUR records:

Model                 ………………………..MC TITAN Pro II      ....…………………………..

Serial No.            ……………………#TP II………………………………………………………..

Purchase Date    ………………………………Please attach a copy of your purchase receipt

Supplier             ……………………………………………………………………………………………………….

Name……………………………………………………….

Address……………………………………………………

Address……………………………………………………

Zip/ Postcode………………………………………….

Country……………………………………………………